## Slide 1
NORDIC FBMC PROPAGATION
Reading the Results
Across the whole app — every tab's output, what it actually says, and the fundamentals that make it trustworthy. Not the interface, the inference.
PTDF & shadow price · fixed effects · clustered SEs · counterfactual impact
Reading the Results · Nordic FBMC Propagation
1

## Slide 2
Agenda
01
Tabs 1–8 — the quick-look results
What a shadow price, a PTDF, a net position, and the map actually mean
02
The fundamentals (Tab 9)
OLS, fixed effects, clustered SEs, p-values, multiple testing — worked, not just named
03
Significant vs. meaningful
Why a p<0.05 result isn't automatically “SUPPORTED”
04
The six verdicts
What each hypothesis tests, and how to read its row — all six worked
05
Per-event results
Reading the ITS chart, ΔRAM decomposition, DiD, and Price Spread
06
Common pitfalls
The ways these results get over-read, across every tab
Reading the Results · Nordic FBMC Propagation
2

## Slide 3
BEFORE WE START
About the Numbers in This Deck
Every worked example here is a real, verified calculation — done by hand or in code — used to teach how the method works.
They are illustrative, not this app's real run output — marked WORKED EXAMPLE throughout
Swap in run_analysis.py's actual numbers once a real run exists; the mechanics you're about to see don't change
Reading the Results · Nordic FBMC Propagation
3

## Slide 4
What's Being Measured
Every hypothesis ultimately traces back to this one identity — seven published terms that sum, exactly, to a CNEC's available capacity.
+
Fmax
Thermal limit
−
FRM
Reliability margin
−
fall
Reference flow
+
fnrao
Allocation offset
+
AMR
Remedial-action adj.
−
FAAC
Frequency-restoration
−
IVA
TSO correction
RAM = Fmax − FRM − fall + fnrao + AMR − FAAC − IVA
H3 asks whether an outage moves this combined total. ΔRAM decomposition asks WHICH of the seven terms actually moved. Both questions only make sense because this identity is verified to balance on real data first.
Reading the Results · Nordic FBMC Propagation
4

## Slide 5
The Other Foundation: PTDF
Power Transfer Distribution Factor — shows up in Tabs 2, 4, 7, and 9. One concept, read differently depending on the tab.
Δflow_{CNEC} = PTDF_{zone,CNEC} × ΔNetPosition_{zone}
Sign
Positive PTDF: a zone importing more pushes MORE flow onto this CNEC. Negative: it pushes LESS — the CNEC is relieved, not stressed, by that zone's imports.
Magnitude
Close to 0: this CNEC barely reacts to that zone's trades. Close to ±1: nearly every MW that zone trades crosses this exact line.
Why it moves
Mostly stable per CNEC — it's topology, not weather. An AC-line outage is the one thing in this study expected to shift it meaningfully (H2's own mechanism).
Where you'll see it
Tab 2's impact formula, Tab 4's own chart, Tab 7 feeds it into ptdf_flow's physics reconstruction, Tab 9's H2 and Price Spread.
Reading the Results · Nordic FBMC Propagation
5

## Slide 6
PART 1
Tabs 1–8 — The Quick-Look Results
Before Tab 9's hypothesis machinery: what every other tab's own output actually means.
Reading the Results · Nordic FBMC Propagation
6

## Slide 7
TAB 1 — FETCH / UPLOAD
The Only “Result” Here Is Data Quality
Tab 1 doesn't produce a verdict — it produces the data everything downstream trusts. Its two checks are the closest thing it has to a result.
RAM-identity balance check — the 7 terms should sum to the published RAM within ~1 MW; a bigger gap means something is wrong with the load, not the outages
Timezone-assumption cross-check (live fetch only) — compares the earliest returned row's raw time against the requested CET calendar-day boundary
Starts near 00:00 raw → consistent with mislabeled-CET data under a “UTC” setting
Starts ~22:00–23:00 the previous day → consistent with genuine UTC data
A warning here isn't a crash — but every downstream tab's numbers inherit whichever assumption was wrong
Reading the Results · Nordic FBMC Propagation
7

## Slide 8
TAB 2 — ANALYSIS
Reading the Impact Table
Reading the Results · Nordic FBMC Propagation
8
impact = shadowPrice × (PTDF_from − PTDF_to)
One row per CNEC, at the exact date+time you picked — an instant snapshot, not a trend
A large |impact| means this CNEC is both binding (nonzero shadow price) AND sensitive to the price difference between your two zones (PTDF gap)
Sorted by |impact| descending — the top row is the single biggest congestion-rent contributor between Zone From and Zone To at that moment
A row missing shadowPrice or either PTDF is excluded from the total, not silently treated as zero — check n_missing in the status line before trusting the total

## Slide 9
TAB 3 — SHADOW / RAM
Shadow Price and RAM, Read Correctly
Shadow price = 0 — this CNEC did NOT bind the market at that moment; the number is exactly zero, not “small,” because non-binding truly costs nothing at the margin
Shadow price > 0 — the CNEC IS binding; the value is the marginal cost, in €/MWh, of relaxing this one constraint by 1 MW
RAM trending toward zero — the CNEC is approaching its limit; watch for the shadow price to switch on right as RAM nears zero
A shadow-price spike with no matching RAM move is worth a second look — check Gen/Cons or Price History for a demand-side driver instead of a capacity one
Reading the Results · Nordic FBMC Propagation
9

## Slide 10
TAB 4 — IMPACT / PTDF
PTDF Sensitivity, Tab by Tab
The same PTDF concept from the foundation slide, now as its own time series.
Mostly flat over time — PTDF is topology, and topology rarely changes minute to minute
A visible step or jump is the signature to look for — that's H2's own mechanism: an AC line outage reshaping the grid
Compare against Tab 3's shadow price at the same timestamp — a PTDF shift only matters economically if the CNEC is also binding
Reading the Results · Nordic FBMC Propagation
10

## Slide 11
TAB 5 — GEN / CONS
Reading Generation vs. Consumption
The supply/demand backdrop — useful for ruling OUT an outage as the cause of something you're seeing elsewhere.
A large generation deficit or surplus in a zone often explains a large net export/import on its own — cross-check against Tab 7's Net Position
If a shadow-price spike or RAM drop lines up with an unusual Gen/Cons swing but NOT with any loaded outage window, the driver is probably demand-side, not maintenance-related
This is the app's main tool for that specific negative check — “is this really about the outage?”
Reading the Results · Nordic FBMC Propagation
11

## Slide 12
TAB 6 — PRICE HISTORY
Realized Price vs. Shadow Price
Two different €/MWh numbers that are easy to conflate — they answer different questions.
Price History (Tab 6): the REALIZED Nord Pool day-ahead price for a zone — what the market actually cleared at
Shadow price (Tab 3): the marginal cost of ONE specific binding CNEC — a component that can feed into price formation, not the price itself
A widening price spread between two zones should generally line up with rising shadow prices on the CNECs between them — if it doesn't, check the CNEC-to-zone mapping before assuming something's wrong
Reading the Results · Nordic FBMC Propagation
12

## Slide 13
TAB 7 — NET POSITION
Reading Net Position
Reading the Results · Nordic FBMC Propagation
13
net position = sell − buy (per zone, per MTU, from Nord Pool's day-ahead Auction Volumes)
Positive — the zone is a net exporter at that MTU; negative — net importer
This is the raw input the ptdf_flow physics-informed method reconstructs 'fall' from: Σ PTDF × NetPosition across zones
Until fetch_nordpool_net_positions() + merge_nordpool_net_positions() are wired into a real-data caller, this feeds only Tab 7's own live chart — not yet Tab 9's regressions on real (non-synthetic) data

## Slide 14
TAB 8 — NORDIC MAP
Reading the Map
The most visually direct result in the app — and the easiest to over-read from one frame.
Color scale = price per zone at that MTU; arrows = flow direction and magnitude between zones
A flow REVERSAL (an arrow flipping direction) between consecutive MTUs is often the single clearest visual signature of an outage's effect
One snapshot can be a blip — use Play to step through the day and check whether a color/arrow change is a persistent shift or a one-off
The map is a sanity-check tool, not a substitute for Tab 9's actual hypothesis tests — it shows you WHERE to look, not whether an effect is statistically real
Reading the Results · Nordic FBMC Propagation
14

## Slide 15
PART 2
Tab 9 — Maintenance Analysis
Where the quick-look reads from Part 1 become a defensible statistical verdict — the fundamentals, all six hypotheses, and every per-event result.
Reading the Results · Nordic FBMC Propagation
15

## Slide 16
FUNDAMENTALS
The Regression Behind Every Verdict
Every H1–H6 result comes from fitting the same kind of line through data and asking how confident we can be in its slope.
y = α + βx + ε
β is the effect size we care about: how much y moves per unit of x. Ordinary Least Squares picks α̂, β̂ to minimize the sum of squared residuals — the line that fits the data best in that specific sense.
WORKED EXAMPLE
Six observations, three before an outage and three during it
β̂ (slope)
−5.333
α̂ (intercept)
100.333
SE(β̂)
1.667
t-statistic
−3.20
p-value (df=4)
0.033
p < 0.05: reject the null that outages don't move this outcome.
Reading the Results · Nordic FBMC Propagation
16

## Slide 17
FUNDAMENTALS
Why Fixed Effects Matter
A CNEC with a naturally low RAM and one with a naturally high RAM differ for reasons that have nothing to do with outages. Left uncorrected, that difference can masquerade as an outage effect.
y_{it} = α_{i} + β D_{it} + ε_{it}
α_i — one fixed effect per CNEC, removed by demeaning each CNEC's own series. What's left, β̂, is identified purely from within-CNEC, before/during comparisons.
WORKED EXAMPLE
Two CNECs, deliberately unbalanced — CNEC A (high baseline) observed mostly BEFORE an outage, CNEC B (low baseline) observed mostly DURING one:
Pooled OLS β̂
−35.8 (confounded)
Ā / B̄ (raw means)
197.8 / 146.0
Fixed-effects β̂
−7.375
SE, t, p (df=7)
1.575, −4.68, 0.0023
Same data, opposite conclusion about the effect's size — pooling let CNEC-level differences leak into β̂.
Reading the Results · Nordic FBMC Propagation
17

## Slide 18
FUNDAMENTALS
Clustered Standard Errors
Observations from the same time period aren't independent — a shock at 14:00 plausibly hits several CNECs at once. Ignoring that overstates how confident a t-stat should be.
WORKED EXAMPLE
SE (naive)
0.151
SE (clustered)
0.262
t (naive)
−51.6
t (clustered)
−29.8
Clustering made the SE 73% larger — the naive t-stat was overconfident.
What this app does about it
Requests time-clustered SEs by default for every H1–H6 fit
Falls back through time → entity → robust → unadjusted if a mode can't be fit
cov_type_used / se_fallback_occurred travel with every result — so a reader can see when it happened
summarize_hypotheses() appends “n=…, se=…” to every verdict
Reading the Results · Nordic FBMC Propagation
18

## Slide 19
FUNDAMENTALS
p-Values, Confidence Intervals, and the Two Errors
β̂ ± t_{α/2, df} · SE(β̂)
p-value
The probability of seeing an effect this large, or larger, if the true effect were zero. Small p ⇒ the data is hard to explain by chance alone.
Confidence interval
The range of β values NOT ruled out at the chosen confidence level. A 95% CI excluding zero is the same statement as p < 0.05, in interval form.
Type I error (α)
Calling a real-zero effect “significant.” Controlled by the significance threshold (0.05) — and by Holm–Bonferroni across six tests, next slide.
Type II error
Missing a real effect. More likely with a short pre-period, few outage episodes, or a noisy dependent variable like shadow price.
Reading the Results · Nordic FBMC Propagation
19

## Slide 20
FUNDAMENTALS
Testing Six Hypotheses at Once
Run six tests at α=0.05 each, and the chance that AT LEAST ONE looks significant by pure luck climbs well past 5%. Holm–Bonferroni corrects for that, in order of strength.
WORKED EXAMPLE
p_{(k)} ≤ α / (m − k + 1) — test in order from smallest p-value, stop at the first failure
Rank (k)
Hypothesis
p-value
Threshold α/(m−k+1)
Outcome
1
H1
0.001
0.05/4 = 0.0125
Reject H₀
2
H4
0.020
0.05/3 = 0.0167
FAIL — procedure stops
3
H3
0.030
—
Not rejected (stopped)
4
H2
0.040
—
Not rejected (stopped)
H2's raw p-value (0.040) would clear an uncorrected 0.05 threshold — but under Holm–Bonferroni it is NOT rejected, because the procedure already failed at H4. This is why the app applies this correction across the whole H1–H6 family, not per-hypothesis.
Reading the Results · Nordic FBMC Propagation
20

## Slide 21
Significant Isn't the Same as Meaningful
A coefficient can clear p < 0.05 and still be too small to matter operationally.
Statistical significance
“This effect is unlikely to be zero.” A property of the estimate's precision — driven partly by sample size.
Economic significance
“This effect is big enough to matter.” A property of the effect's SIZE, judged against ECONOMIC_SIGNIFICANCE_THRESHOLDS — a documented, conservative floor per dependent variable.
A hypothesis that clears p<0.05 but not its economic floor is reported “statistically significant,” never “SUPPORTED.” That distinction is why H3's sample verdict later in this deck reads “SIGNIFICANT*” rather than “SUPPORTED.”
Reading the Results · Nordic FBMC Propagation
21

## Slide 22
The Six Hypotheses
Each isolates one specific channel from a specific outage type to a specific CNEC parameter.
Outage type
Parameter tested
Mechanism
Status
H1
HVDC outages
→
Reference flow (fall)
Direct physical rerouting
Tested
H2
AC line outages
→
PTDF sensitivity
Topology change
Tested
H3
Forced outages
→
RAM (combined)
Net capacity impact
Tested
H4
Forced outages
→
Shadow price
Binding-constraint cost
Tested
H5
Outage type
→
IVA (logit)
TSO discretionary use
Tested
H6
Any outage
→
FRM (placebo)
Should show NO effect
Null expected
Reading the Results · Nordic FBMC Propagation
22

## Slide 23
How to Read a Verdict Row
Every H1–H6 result is one row with the same seven fields — here's what each one is answering.
β̂ (coefficient)
Direction and rough size of the effect — sign tells you increase vs. decrease
SE (clustered)
How precisely β̂ is estimated — smaller is more precise, given the same β̂
t / z-statistic
β̂ divided by SE — how many standard errors away from zero
p-value
Probability of a t-stat this extreme if the true effect were zero
n
Sample size actually used — watch for this shrinking on a binding-only subsample (H4)
Verdict
SUPPORTED (clears both bars) · SIGNIFICANT-only (p<0.05, misses economic floor) · NOT SUPPORTED · NULL (H6, as expected)
Reading the Results · Nordic FBMC Propagation
23

## Slide 24
H1
HVDC Outages → Reference Flow
Reading the Results · Nordic FBMC Propagation
24
The most direct, physical channel in this study: a cable goes down, flow reroutes. Shown here as a single CNEC's before/during comparison for clarity — the real fit pools every matched CNEC with fixed effects and clustered SEs, same machinery as every other hypothesis.
WORKED EXAMPLE
4 pre-outage vs. 4 during-outage readings of fall_signed (MW)
α̂ (pre-outage mean)
619.5
β̂ (change)
−35.5
t-statistic (df=6)
−10.91
p-value
0.000035
Verdict: SUPPORTED — the reference flow drops by ~35.5 MW during the outage, a shift far too large to be noise (p ≈ 0.00004) and well past this variable's economic floor.

## Slide 25
H2
AC Outages → PTDF Sensitivity
Reading the Results · Nordic FBMC Propagation
25
Uses the ABSOLUTE PTDF value — the specification choice that makes this a clean test of a pure topology effect: an AC line outage changes the grid's shape, which can push a CNEC's sensitivity up or down depending on where it sits, not in one fixed direction.
WORKED EXAMPLE
β̂₂
0.00983
SE (clustered)
0.00098
t-statistic
10.00
p-value (df=9)
<0.0001
Verdict: SUPPORTED — tiny p-value, and the coefficient clears its economic floor (a topology shift moving PTDF by this much is operationally meaningful).

## Slide 26
H3
Forced Outages → RAM
Reading the Results · Nordic FBMC Propagation
26
Because RAM is the seven-term identity, a significant β̂₃ says the COMBINED, already-netted effect across every term moved — it doesn't say which term. That's what ΔRAM decomposition is for. Worked with fixed effects across three CNECs, so the panel machinery is visible directly.
WORKED EXAMPLE
3 CNECs × 4 periods (2 pre, 2 during), RAM in MW — fixed-effects (within) estimator
Pooled β̂ (no FE)
−32.17
β̂₃ (fixed effects)
−32.17
SE (df=8)
1.845
t, p
−17.44, <0.0001
Pooled and FE estimates agree here because the three CNECs' baselines are close together — unlike the omitted-variable-bias demo earlier, where they didn't. Verdict: SUPPORTED, and the ~32 MW average RAM loss clears the economic floor — ΔRAM decomposition (later) is what tells you WHICH of the seven terms drove it.

## Slide 27
H4
Forced Outages → Shadow Price
Reading the Results · Nordic FBMC Propagation
27
Fit on the BINDING SUBSAMPLE only — rows where the CNEC actually has a positive shadow price — since a non-binding CNEC's shadow price is exactly, structurally zero, not just small. Including those rows would dilute the estimate with a floor effect, not real variation.
WORKED EXAMPLE
β̂₄
11.75
SE (clustered)
1.328
t-statistic
8.85
p-value (df=5)
0.0003
n here is smaller than H1–H3's — the binding subsample is a fraction of all rows. Watch n alongside the verdict: a striking β̂ on very few binding rows deserves more scrutiny than the same β̂ on hundreds.

## Slide 28
H5
IVA → Logistic Regression
Reading the Results · Nordic FBMC Propagation
28
IVA is usually exactly zero, so H5 can't be a linear regression on IVA's SIZE the way H1–H4 are — it's a logit on whether IVA is used AT ALL, comparing forced vs. planned outages.
ln( p / (1−p) ) = γ₀ + γ₁ · Forced
WORKED EXAMPLE
γ̂₀ (intercept)
−1.386
γ̂₁ (Forced)
2.773
P(IVA | planned)
0.20
P(IVA | forced)
0.80
z = 1.75, p = 0.080 — doesn't clear the 0.05 bar. Verdict: NOT SUPPORTED, despite forced outages showing 4× the predicted probability of IVA use — a small-sample story, not a null effect story.

## Slide 29
H6
FRM — The Placebo
Reading the Results · Nordic FBMC Propagation
29
Same specification family as H1–H4, fit on FRM — a STRUCTURAL, yearly-calibrated quantity that should be inert to any single outage. This is the one hypothesis where NOT rejecting H₀ is the desired outcome.
WORKED EXAMPLE
β̂₆
−0.033
SE (clustered)
0.113
t-statistic
−0.294
p-value
0.775
p = 0.775: nowhere near significant. Verdict: NULL, as expected — this is the test PASSING, not a weak result. If H6 ever came back significant, that would call the whole specification into question.

## Slide 30
PER-EVENT RESULTS
Reading the ITS Chart
A different question from H1–H6: not “do outages move this on average,” but “what happened at THIS one outage.”
Chart: 
| -72h | -48h | -24h | outage start | +24h | +48h | +72h
Actual | 812 | 805 | 795 | 640 | 610 | 690 | 770
Counterfactual Y(0) | 808 | 800 | 798 | 802 | 799 | 795 | 801
WORKED EXAMPLE
Counterfactual = what this CNEC's series would look like WITHOUT this outage, fit on pre-period data only
The GAP between the lines during the outage IS the estimated effect — not a statistical test, a direct read
The gap should close again once the outage ends — if it doesn't, something else may be going on
Every method is leak-tested: it can never see during/post data while fitting
Reading the Results · Nordic FBMC Propagation
30

## Slide 31
PER-EVENT RESULTS
Reading ΔRAM Decomposition
The ITS chart tells you RAM moved. This pane tells you WHICH of the seven identity terms did the moving.
Each term gets its own before/during comparison — Fmax, FRM, fall, fnrao, AMR, FAAC, IVA
A dominant single term (usually fall, for a topology-driven outage) points to a physical, expected mechanism
Several terms moving in OFFSETTING directions explains why H3's aggregate β̂ can look modest even when the underlying activity was large
FRM moving here (rather than staying flat) would be a red flag — it's meant to be structural, the same logic H6 tests at the aggregate level
Reading the Results · Nordic FBMC Propagation
31

## Slide 32
PER-EVENT RESULTS
Reading the DiD Cross-Check
A second, independent identification strategy for the SAME event: high-PTDF_FI CNECs vs. low-PTDF_FI CNECs, before vs. during.
If a CNEC's PTDF to the source country is high, an outage there should hit it harder than a low-PTDF CNEC — that differential IS the DiD estimate
Agreement with the ITS result is reassuring — two different methods reaching the same conclusion
Disagreement is worth investigating, not dismissing — check whether the “high vs. low” PTDF split is even meaningful for this specific CNEC set
Reading the Results · Nordic FBMC Propagation
32

## Slide 33
PER-EVENT RESULTS
Reading the Price Spread Output
impact = (shadowPrice × PTDF)_actual − (shadowPrice × PTDF)_counterfactual
Actual
Both factors, at the picked timestamp, as observed
Counterfactual
Both factors' own ITS projection, same timestamp
Impact
The difference — this CNEC's own contribution shift
Both shadowPrice AND the target zone's PTDF get their own ITS counterfactual — PTDF itself can shift during an AC-line outage on the target zone, the same mechanism H2 tests for. This is ONE CNEC's own change in contribution, not the full zonal price move — the real total sums this same term over every binding CNEC.
Reading the Results · Nordic FBMC Propagation
33

## Slide 34
Common Pitfalls, Across Every Tab
!
Reading a Nordic Map snapshot as proof — one MTU can be a blip; use Play to check it persists
!
Conflating Tab 6's realized price with Tab 3's shadow price — they answer different questions
!
Treating p < 0.05 alone as “proven” — always check the economic-significance floor too
!
Reading H2's raw p-value in isolation — Holm–Bonferroni can still block it if a stronger hypothesis already failed
!
Ignoring n — a striking coefficient on very few binding rows (H4) deserves more scrutiny, not less
!
Treating an ITS gap as automatically causal — check the gap closes again after the outage ends
!
Assuming a weaker-than-requested SE fallback is the same as the requested one — check se_fallback_occurred
!
Reading Price Spread's impact as the FULL zonal price move — it's one CNEC's own contribution only
!
Hoping H6 comes back significant — for the placebo, null IS the good result
Reading the Results · Nordic FBMC Propagation
34

## Slide 35
Go Deeper
1
Understanding the Maintenance Analysis Tab (docx / pdf)
56-chapter learner's guide — full derivations, every hypothesis worked, diagnostics, a full case study
2
Summary Edition (pdf)
29-page condensed version — same chapters, opening idea + central formula each
3
Nordic_FBMC_App_Tour.pptx
The companion deck for setup/UI — every tab, sub-tab, and control, if you need the interface too
4
MAINTENANCE_TAB_GUIDE.md
Focused guide to Tab 9, its state and gotchas
5
test_pipeline.py
Leak-safety and regression tests — the proof these methods behave as described
Reading the Results · Nordic FBMC Propagation
35