## Slide 1
NORDIC FLOW-BASED PROPAGATION
Does a Maintenance Outage in One Zone
Move Another Zone's CNEC Parameters?
A panel-regression and counterfactual (ITS) study of Nordic day-ahead flow-based capacity calculation, with a worked example price-impact calculator.
Results shown in this deck are SAMPLE / ILLUSTRATIVE data for slide design — replace with the real run's output before presenting.

## Slide 2
Agenda
01
Why this matters
Cross-border propagation risk in Nordic FBMC capacity calculation
02
How we test it
Panel regression (fixed effects, clustered SEs) + counterfactual ITS modeling
03
The six hypotheses
H1–H6, each isolating one channel from outage to CNEC parameter
04
Sample results
Illustrative verdicts, coefficients, and a single-event counterfactual
05
Price-impact calculator
Turning a shadow-price shift into a zonal price effect
06
Next steps
What changes once real JAO/ENTSO-E data replaces these placeholders
Nordic Flow-Based Propagation · fi_no3
2

## Slide 3
Flow-Based Market Coupling, in One Picture
Every Critical Network Element (CNEC) gets a capacity budget (RAM) built from seven published terms — an outage anywhere on the grid can move any of them.
+
Fmax
Thermal limit of the line
−
FRM
Reliability margin (structural)
−
fall
Reference flow (F_allReference)
+
fnrao
Non-redundant allocation offset
+
AMR
Adjustment for remedial actions
−
FAAC
Frequency-restoration allocation
−
IVA
TSO discretionary correction
RAM = Fmax − FRM − fall + fnrao + AMR − FAAC − IVA
This tab verifies that identity balances to within ~1 MW on real published data, then asks: which term(s) does an outage actually move, and by how much?
Nordic Flow-Based Propagation · fi_no3
3

## Slide 4
Method 1 — Panel Regression Across Outages
Pools every outage episode to ask: does this TYPE of event move this parameter, on average, across the whole sample?
The specification
y_{it} = α_{i} + β D_{it} + ε_{it}
α_i — CNEC fixed effect (within-transform / demeaning removes it)
D_it — outage-active dummy or MW-lost dose variable
Standard errors clustered by time period (sandwich estimator)
Holm–Bonferroni correction across the H1–H6 family
Why fixed effects matter
A CNEC with a naturally low RAM and a CNEC with a naturally high RAM will differ in level for reasons that have nothing to do with outages. Demeaning each CNEC's series removes that between-CNEC variation entirely, so β̂ is identified purely from within-CNEC, before/during comparisons — the same logic as a CNEC-level difference-in-differences.
Omitted-variable-bias illustration (worked example)
Pooled OLS: β̂ = −35.8 (confounded by level differences)
Fixed effects: β̂ = −7.4, SE = 1.6, t = −4.7, p = 0.002
Nordic Flow-Based Propagation · fi_no3
4

## Slide 5
Method 2 — Counterfactual (ITS) Modeling
Asks a sharper, single-event question: what would this CNEC's parameter have looked like WITHOUT this specific outage?
Chart: RAM around a forced outage — one CNEC
| -72h | -48h | -24h | outage start | +24h | +48h | +72h
Actual | 812 | 805 | 795 | 640 | 610 | 690 | 770
Counterfactual (fit on pre-period only) | 808 | 800 | 798 | 802 | 799 | 795 | 801
SAMPLE DATA
Reading the chart
Fit on pre-outage data only — never touches the during/post window
13 methods available (seasonal-naive → SARIMA → ensemble → physics-informed)
Gap between the two lines during the outage = the estimated impact
Gap should close again once the outage ends
Nordic Flow-Based Propagation · fi_no3
5

## Slide 6
The Six Hypotheses
Each isolates one specific channel from a specific outage type to a specific CNEC parameter.
Outage type
Parameter tested
Mechanism
Status
H1
HVDC outages
→
Reference flow (fall)
Direct physical rerouting
Tested
H2
AC line outages
→
PTDF sensitivity
Topology change
Tested
H3
Forced outages
→
RAM (combined)
Net capacity impact
Tested
H4
Forced outages
→
Shadow price
Binding-constraint cost
Tested
H5
Outage type
→
IVA (logit)
TSO discretionary use
Tested
H6
Any outage
→
FRM (placebo)
Should show NO effect
Null expected
Nordic Flow-Based Propagation · fi_no3
6

## Slide 7
Sample Results — Hypothesis Verdicts
SAMPLE DATA
FI → NO3, illustrative 90-day window — replace every number below with the real run's summarize_hypotheses() output.
Hyp. | Coefficient (β̂) | SE (clustered) | t-stat | p-value | n | Verdict
H1 | −4.82 | 1.40 | −3.44 | 0.0021 | 312 | SUPPORTED
H2 | 0.0098 | 0.0010 | 9.80 | <0.0001 | 289 | SUPPORTED
H3 | −6.15 | 3.02 | −2.04 | 0.048 | 312 | SIGNIFICANT*
H4 | 11.75 | 1.33 | 8.85 | 0.0003 | 94 | SUPPORTED
H5 | 2.77 | 1.58 | 1.75 (z) | 0.080 | 312 | NOT SUPPORTED
H6 | −0.033 | 0.113 | −0.29 | 0.775 | 312 | NULL (as expected)
* Statistically significant but reported separately from “SUPPORTED” where it does not clear the economic-significance floor — see ECONOMIC_SIGNIFICANCE_THRESHOLDS.
Nordic Flow-Based Propagation · fi_no3
7

## Slide 8
Sample Results — Effect Sizes at a Glance
SAMPLE DATA
Chart: Standardized coefficient
| H1: fall | H2: ¦PTDF¦ | H3: RAM | H4: shadow € | H5: IVA logit | H6: FRM (placebo)
β̂ (standardized) | -0.61 | 0.58 | -0.34 | 0.71 | 0.22 | -0.03
Nordic Flow-Based Propagation · fi_no3
8

## Slide 9
From CNEC Parameters to a Zonal Price Effect
The Single-Event tab's Price Spread pane turns a shadow-price / PTDF shift on one CNEC into an actual-vs-counterfactual price impact for a target zone.
impact = (shadowPrice × PTDF)_actual − (shadowPrice × PTDF)_counterfactual
Actual
Shadow price: 18.4 €/MWh
PTDF (target zone): 0.28
Counterfactual
Shadow price: 6.1 €/MWh
PTDF (target zone): 0.24
Impact
+3.6 €/MWh
on the target zone
SAMPLE DATA
Refuses to compute (rather than guess) when the target PTDF column is missing, the pre-period has fewer than 4 distinct timestamps, or no row falls within tolerance of the requested time.
Nordic Flow-Based Propagation · fi_no3
9

## Slide 10
Sample Results — Robustness Checks
SAMPLE DATA
Clustering choice
Time-clustered vs. entity-clustered SE agree within 15% on every H1–H4 verdict
Pre-period length
H4's β̂ stable (±8%) across 30/60/90-day pre-period windows
Placebo (H6)
FRM shows no significant movement — the null the project wants to see
Collinearity
Dummy/dose pairs pruned automatically where near-collinear (H1, H3)
Residual diagnostics
Durbin–Watson ≈ 1.9–2.1 across specifications — no strong autocorrelation
ITS leak check
Counterfactual projections verified not to touch during/post data
Nordic Flow-Based Propagation · fi_no3
10

## Slide 11
Next Steps
1
Swap in the real run: replace every SAMPLE-badged number with run_analysis.py's actual output
2
Widen the sweep: run --all-nordic-zones for the full Nordic source × target matrix, not just FI → NO3
3
Cross-check ITS method choice: compare seasonal-naive / ensemble / physics-informed projections on the real pre-period
4
Re-run the price-impact calculator on a real binding CNEC once real shadow-price data is loaded
Nordic Flow-Based Propagation · fi_no3
11